## Slide 1: PythonUDS
A semi-detailed overview

## Slide 2: What is PythonUDS?
It is a high level Unified Diagnostic Service (UDS) client for Python
Written to be used by both hobbyist and professional users
Supports industry standard hardware interfaces (Vector, Peak Systems, National Instruments) and the ASAM Open Diagnostic Exchange format (ODX)

## Slide 3: What is UDS?
UDS (Unified Diagnostic Service) is a protocol to communicate with (typically) automotive ECUs.
It has been around for a long time, so most likely everyone’s car supports it
Can be used on most automotive physical layer systems (CAN, LIN, Ethernet, DoIP, FlexRay, K-Line)
Used for generally any interaction to control an ECU, from resetting DTCs to flashing new firmware images

## Slide 4: Why should you care what UDS is?
If you ever want to tinker with vehicle data, UDS provides a nice interface
  Easier to interface with than having to reverse engineer raw CAN data (This can be simple, but can also be incredibly complex)
There are standard parameters for some data such as; engine speed, engine temp, throttle position, fuel trim, etc (links later)
UDS data can also help when identifying raw CAN data to provide references from trusted data sources
You can read and clear DTCs (the scourge of modern cars!)

## Slide 5: Why create PythonUDS?
There are a number of very good OTS solutions (CANalyzer, CANoe, CANape, Bosch ETAS) but they are all VERY expensive
  Prices range from a few £1000, to £10000+ depending on the functionality
There are a number of open source python UDS clients but they all have a common problem… Hardware incompatability!
  They either support 1 specific protocol (usually CAN) or they only work on 1 type of hardware interface (usually Linux socketcan or peak systems)
The goal was to create a high level interface that could easily be adapted to a variety of physical network types and hardware interfaces
I had to do something for my Open University final project…
  This was the least risky concept

## Slide 6: General Info / Context
Stuff about UDS & cars

## Slide 7: Electronic Control Units (ECUs)
A modern car can have upwards of 20 individual ECUs and 3 communication bus
  A modern Land Rover Discovery has 50+ ECUs, 6 CAN bus, 1 FlexRay bus and a DoIP (automotive ethernet) diagnostics connection (there are actually more networks as well….)
For CAN (which is the most common) each ECU is given two unique addresses. The Request ID (Tx) and Response ID (Rx)
  For an engine ECU this is: 0x7E0 (Tx) and 0x7E8 (Rx)
  For a transmission ECU this is: 0x7E1 (Tx) and 0x7E9 (Rx)
ECUs can also listen to the broadcast ID 0x7DF (Tx) and will respond on their own Response ID

## Slide 8: UDS ECUs and Testers
UDS classifies endpoints as Servers (Typically ECUs) or Testers / Clients (Diagnostic equipment)
Servers can not initiate communications on their own
  There are instances of ECUs using UDS to talk to each other, but this is generally non-standard and there are other protocols that better solve this need
A tester is the tool that a garage will use to communicate with the ECUs
  This is typically an (overpriced) laptop with a (very overpriced) hardware interface, but there are handheld versions for simple diagnostics
There are also UDS gateways but these are usually transparent
  Typically used to present 1 interface to multiple networks

## Slide 9: UDS Messages
UDS messages have a common format
This is an example of the OBD-II(1) Mode 1 Engine Speed Parameter
  Request: 01 12 1F 40
  Response: 41 12 1F 40
  Green is the service
  Yellow is the response code(2)
  Blue is the mode
  Orange is the Data
  In this example the scaling is simply y=0.25x
  which in this example is 2000 rpm
(1) OBD (on-board diagnostics) is an industry standard protocol built on UDS. Look at https://en.wikipedia.org/wiki/OBD-II_PIDs for more information
(2) A valid response adds 0x40 to the service request (0x01 -> 0x41).
An invalid response is 0x7F which represents an error. The error code is then included in the payload.
There are other responses but they are more complex and generally relate to flow control so we’ll skip these

## Slide 10: UDS Services and DIDs
There are a large number of services defined
  0x01 – 0x0A are standardised by the OBD-II standard and include basic diagnostic information, manufacturers have to conform to the exact structure of the service and its parameters
  0x10 upwards are partially standardised
    IDs are fixed to certain purposes (read data = 0x22, write data = 0x2E, remote IO = 0x2F)
    The content is more flexible and parameters are optional
Diagnostic Identifiers (DIDs) are used to represent individual parameters
  DIDs are common across services
  There are some standardised DIDs (Serial Number, software version number etc) but these are up to the manufacturer to define

## Slide 11: Transport Protocols
Most of the automotive communications networks were not designed for high bandwidth
  CAN / LIN both have an 8 byte payload
  FlexRay and Ethernet can utilise larger payloads but still sometimes rely on transport protocols)
This means that most useful data must be transmitted and received across multiple messages

## Slide 12: CAN Transport Protocol – Example
The message to set the ECU serial number:
2E F1 8C 01 02 03 04 05 06 07 08 09 0A 0B 0C 0D 0E 0F
Is too long for 1 CAN payload, so the transport protocol would split it into several.
It starts with a “First Frame” from the sender
10 12 2E F1 8C 01 02 03
The “Flow Control” from the receiver gives the information about how to send the rest of the data (not covered here but it specified timing and sizing for the remaining consecutive frames)
30 10 05 00 00 00 00 00
The sender would then send “Consecutive Frames” until the paylod is sent
21 04 05 06 07 08 09 0A 0B
22 0C 0D 0E 0F
This way CAN is able to transmit up to 4095 bytes in a single UDS message, larger messages need a further transport protocol (there are standardised functions for transmitting configuration or programming ECUs which generally have 1 - 3 Mb of ROM)
Legend
Green = Message type
Blue = Total Payload Size
Dark orange = Payload
Red = Block size
Purple = Min timing interval
Black = Seqence number

## Slide 13: Python-UDS Structure

## Slide 14: Overall System Architecture
High level UDS class (high-level – User facing)
  Used to represent the connection to the ECU itself, send and receive UDS messages
Transport Protocols (mid-level)
  Used to break-up and re-combine UDS messages from the underlying communications protocol
Communications Interface (low-level)
  Used to set up the physical connections as well as transmitting and receiving data
UDS Config Tool - A builder (ish) for constructing extra methods for the UDS class

## Slide 15: UDS Class
Quite basic, simply sends and receives messages from the lower levels
Handles interpreting the response code
Has one method send(msg)which returns a response or raises an exception if the message fails

## Slide 16: Transport Protocols
The design calls for flexible interfaces, so a factory pattern was adopted with a standardised interface; send and recv
Currently the design supports two transport protocols which are very similar; CanTp and LinTp
For the initial project only CanTp was supported. LinTp was added later to support a new customer.

## Slide 17: Communication Interfaces
Python-CAN is an open source project which provides a common interface for a number of industry standard hardware interfaces
  This was a perfect choice for the project
  Currently the CanTp class has a very tightly coupled interface to this library but the intent is to break it out to add TP capabilities to non-supported interfaces
Python-LIN was created to provide a similar library to Python-CAN but is in development. It currently only works with Peak Systems LIN interfaces
  Support for Vector interfaces is in progress
  Development of a cheap LIN master interface hardware is (in very early) development

## Slide 18: Other little things - Config and Kwargs
One problem that appeared early on was the need to pass complex parameters to constructors lower down in the hierarchy
  The solution was a series of config files and liberal use of the python keyword arguments (kwargs)
Configuration for the classes comes in 4 parts;
  Mandatory params – Must be there to instantiate a class
  Default config files – Contain default, non-mandatory config
  User config files – User created configuration files which can specify a number of different parameters
  Kwargs – User specified configuration from the UDS class constructor
The default config can be found in each class directory and just defines the basic config for each class
A config file specified by the user can be passed from UDS constructor and this supersedes the default config
Kwargs corresponding to each config item can be passed down from each level to override the config file
This gives a lot of configurability

## Slide 19: UDS Config Tool
Taking ODX files and creating functions

## Slide 20: UDS Config Tool (Terrible name)
Industry tools such as CANDela are used to generate diagnostic databases which define exactly the UDS messages
These are high level and really easy to understand and can be output into a standardised XML format (ASAM ODX)
The ODX parser basically takes the ODX file and autogenerates a set of functions to interface with the UDS messages
  Constructs UDS messages from human readable text
  Interprets UDS messages into human readable text
These methods are then added to the base UDS object so that it can reference them as methods

## Slide 21: UDS Config Tool - Example
If I wanted the engine speed (DID 0x1000) from the Read Data by Identifier service (Service 0x22)
  Just using the python-uds base methods
    engine_speed = ecu.send([0x22, 0x10, 0x00,])
    print(engine_speed) -> [0x61, 0x10, 0x00, 0x1F, 0x00]
    This is a little clunky as the user then has to recombine the data before it is useful
  Using the ODX Parser (assuming the parameter is defined as “Engine Speed”
    engine_speed = ecu.readdatabyidentifier(“Engine Speed”)
    print(engine_speed) -> {“Engine Speed”: 2000}
    This is much easier and more convenient

## Slide 22: UDS Config Tool – Service Methods
Service functions are pre-defined and have a fixed interface
Each service has a method factory which dynamically creates the DID functions and adds them to the dictionaries for each service function
Once complete these service functions are then bound to the UDS instance
  This allows the UDS instance to then call them as methods of the class

## Slide 23: UDS Config Tool – DID Methods
These are the dynamically created functions created from the ODX XML file (The XML structure is fairly obtuse so I won’t go through any here)
There are 4 functions created for each DID or Service Instance:
  Request Function – Prepares the request to be sent to the server
  Negative Response Function – Parses the response for a negative response
  Check Function – Checks the response for basic correctness, length etc
  Positive Response Function – Parses the response payload and decodes into a dictionary
These functions are executed in sequence and if a problem occurs at any point it raises an exception

## Slide 24: UDS Config Tool - Why bother?
The format of the diagnostic databases can be very complex
Engine Speed is a DID with 1 parameter which is a single data-type
  This is probably the simplest case
Each DID can have any number of parameters of any data-type supported by the ODX standard (strings, floats, bit-fields, enumerations)
  This would be very tiring for the user to have to write functions to deal with all of these on a case-by-case basis
For hobbyists it isn’t so bad as they are usually working with a limited set of vehicles
Professionals vary in technical competence, so the tool presents a common, easy to reference format for them to interrogate their ECUs

## Slide 25: Testing
The bit everyone LOVES talking about

## Slide 26: Testing Methodology
The overall development cycle was waterfall based with three tiers:
  Functional Tests – Highest level
  Integration Tests – Integration between two components
  Unit Tests – Tests a single method. Uses the python mock library
The plan was that the code should be developed with extensive unit tests using TDD principals.
  The code was written such that it should be unit testable, breaking functions down into small manageable chunks
  This was not strictly followed and there is very little unit test coverage of some parts of the code
  Some code was developed in a TDD fashion but this was found to be quite difficult to follow rigidly as the requirements were not very granular

## Slide 27: CI / CD
Due to the nature of the dynamic function generation a CI / CD pipeline was an obvious diagnostic choice
There is a need to have an ECU in-the-loop which is complicated
  Real ECUs would require a dedicated system to run the CI/CD system as it would need access to the hardware
  There isn’t an Open Source / Free Virtual ECU which supports UDS
  It was not wise to use an instance of python-UDS to act as the virtualised ECU as this may have compounded errors

## Slide 28: Conclusions
Was it really worth it?

## Slide 29: Conclusions
The code was very successful at Embed
  Replaced older in-house tools
  Used by staff in place of industry tools
  Integrated into customer projects, including OEM vehicle manufacturers
Improvements to the code were fairly easy
  Addition of the LinTp and Interface code took about 1 week
  Addition of socketCAN and linux support took 1 evening
Had feedback / improvements from several people on GitHub
Really interesting to create and learned a lot about python unit-testing and supporting python features (PIP and python packages)

## Slide 30: The Future!
What to do next!

## Slide 31: The Future!
Python-UDS
  Decouple CanTp and LinTp from their hardware implementations
  Implement a software interface to cheaper CAN hardware (https://www.macchina.cc/catalog)
Python-LIN
  Develop into a more complete solution
  Create a LIN master hardware interface to enable UDS on LIN for less cost
Other
  Write an ODX generator to enable hobbyists to define their own databases

## Slide 32: Parts – If you want to give it a try
An easy way to get started is with a raspberry pi
  Can easily fit in a car
  Nice screen options for permanent integration projects
Raspberry Pi 4 – https://cpc.farnell.com/raspberry-pi/rpi4-modbp-2gb-bulk/raspberry-pi-4-model-b-2gb-bulk/dp/SC15186
Pi CAN Hat (necessary to interface with CAN) - http://skpang.co.uk/catalog/pican2-canbus-board-for-raspberry-pi-2-p-1475.html
Screen (optional, this one is expensive but good) - https://thepihut.com/collections/raspberry-pi-screens/products/official-raspberry-pi-7-touchscreen-display
Smaller Screen (still good but much smaller) - https://thepihut.com/collections/raspberry-pi-screens/products/adafruit-pitft-2-8-touchscreen-for-the-raspberry-pi

## Slide 33: Links & Info
Python-UDS source: https://github.com/richClubb/python-uds
Python-UDS docs: https://python-uds.readthedocs.io/en/latest/index.html
Hackaday has a good series on CAN hacking
  https://hackaday.com/2013/10/21/can-hacking-introductions/
OBD-II PIDs
  https://en.wikipedia.org/wiki/OBD-II_PIDs
UDS ISO standard - ISO-14229 (boring but comprehensive)
CAN Transport Protocol standard – ISO-15765 (very boring)